Architectural Guidelines

# integrated pest management – Design condiserations for schools

## Developed in consultation with Safer Pest Control Project, Gregg

## Smith (Salt Lake City School District) and David L.

## Shangle  B.C.E., Dalsh Consulting

Below are general design and construction guidelines for discouraging a variety of arthropod and vertebrate pests.  You can establish more specific guidelines by determining the pests that are typical in your area, and undertake building design with them in mind.

- Entrance Ways –

  - Outside doors outfitted with door sweeps that fit snugly against the threshold and are flush with the doorframe on both sides.  Sweeps can be either the brush or rubber variety.

  - Weather-stripping on doorframe along both sides and top of frame.

- Windows –

  - Incorporate windows which can accommodate screens.

  - Screens that are taught, without tears, and sealed tightly around the frame with a gasket.

  - Use aluminum, 10 mesh or smaller (aluminum can be stretched more tightly).

  - Weather stripping around window frame for a tight seal.

- Caulking/Sealing – eliminate holes, cracks, crevices, and gaps:

  - Larger holes (pipe openings, etc.): stuff steel wool inside, and then fill with mixed cement or quality butyl caulk.

  - Smaller openings: should be caulked and/or sealed using elastomeric silicone sealant.

    - Throughout Building:  along baseboards, floor and wall joints, window and door moldings, edges of electrical outlet covers, and radiator covers.

    - Pipes/Wiring: around all water, electrical pipes, cable and/or other wires coming into a unit.

    - Kitchen/Bathroom:  around sink edges, where cabinets and countertops meet walls (particularly under the sink), between cupboards and countertops.

- Landscaping – trees, shrubs, and ornamentals that are:

  - At least 1’ away from the building.

  - Spaced far enough apart for 1’ separation at full growth.

  - Leaves, branches that have some ground clearance.

- Outside Air Intakes/Vents – screened with 10 mesh or smaller; fabricated and installed to be easily removed for cleaning.  Area to consider:

  - Foundation Vents: many vents are constructed with screens; one should be fabricated for those that are not.

- Floor Drains – Course mesh screens or floor sink baskets should cover drains or sunken floor drain baskets.   Covers or baskets must be removable for cleaning.

General Design Tips

Avoid:

- Nooks and flat ledges

- Lights above doorways; use reflected light to illuminate doorways

- Vegetation against the building (this includes grass)

- Pipes, electrical conduits, or hoses against walls

- Pipes entering drains that prevent drain maintenance

- Inaccessible drains under fixed kitchen equipment

- Equipment legs in inaccessible corners (corner-cleaning must be as easy as possible)

Limit:

- Alcove areas, which gather debris and serve as pest harborage areas

Use:

- Sloped or rounded decorative ledges and/or window frames

- Outdoor lights positioned away from entrances

- Non-vegetative boarders against buildings (gravel, etc.)

- Downspouts should be mounted 4-6 inches from building sides using spacers

- Concrete turf boarders at turf level so grass mowers can mow over them

- Self-closing trash cans which are elevated off the ground and set in a concrete slab

Build Pests Out 
so we can keep our kids in!